## Slide 1: Rethinking Cache Hierarchy and Interconnect Design for Next-generation GPUs
Mohamed Assem Ibrahim
Ph.D. Candidate
https://massemibrahim.github.io/

## Slide 2
2X Transistors / 18-24 Months
Higher Frequencies at the Same Power
Slowing Moore’s Law
Power Wall
1) Moore’s Law
2) Dennard Scaling
Diminishing Benefits!
High Performance
Solution?
Hennessy & Patterson, “A New Golden Age for Computer Architecture.” Communications of the ACM 2019.

## Slide 3
[Micron] Automata Processor
[Microsoft] Catapult
[Google] Tensor Processing Unit
[Google] Pixel Visual Core
Domain Specific Architecture (DSA)

## Slide 4
Graphics Processing Unit (GPU)

## Slide 5: From DSA to General-purpose Architecture
General-purpose Applications
Machine
Learning
Physics
Simulation
Image/Audio Processing
Financial Computing
Genomics
High Data-Level Parallelism
General-purpose Applications
Multi-threading Capability
General-purpose Computing on GPUs (GPGPUs)
Execution Unit
Astronomy
Medical
Imaging
Content Creation
Games
High Data-Level Parallelism

## Slide 6: GPUs are everywhere!

## Slide 7: How Acceleration Works?
CPU
GPU
Few Cores
Optimized for Latency
Great for Sequential Code
Large Number of Cores
Optimized for Throughput
Great for Parallel Code
Application Code
Sequential Code
Parallel Code
Sequential Code
Core
Core

## Slide 8: State of GPU Computing Application Trends
Large workloads/datasets.
Multi-application execution.
Increasing Computational Demand

## Slide 9: State of GPU Computing Hardware Trends
GPU die sizes are getting larger.
Core count is increasing as well.
Chart: Year
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2013 | 2015
Area | 70 | 97 | 68 | 218 | 218 | 297 | 288 | 352 | 420 | 282 | 334 | 389 | 365 | 438 | 596
Wikipedia (Data)

## Slide 10: Problem?
Memory Wall
Processor
Memory
Processor-Memory Performance Gap
Moore’s Law
Year
Performance
Compute Boost is limited by Memory Bandwidth

## Slide 11: Solution?
…
Register File
L1$
Scratchpad
PE
PE
GPU Core
NoC
Memory
L2$
Memory Partition
Not Enough!
On-chip Caching Resources

## Slide 12: Scale Bandwidth Resources?
1) Cost Limitation
2) Power Limitation
3) I/O Limitation

## Slide 13: Dissertation Statement
Improve On-chip Memory Bandwidth Utilization
to Enable the Next-generation of GPUs
Via Rethinking Cache Hierarchy & Interconnect

## Slide 14: Outline
Conventional Cache/Interconnect Hierarchy
Dissertation Research
Conclusions & Future Work

## Slide 15: GPU Architecture
Assign Work  GPU Core
  Function (Kernel) + Data
Run Threads  PEs
  PE = Processing Element
Read/Write Data?  LD/ST Unit
  LD/ST = Load/Store
Coalesce Read Requests
Check L1 Cache
Read Request Pending?  MSHR
  MSHR = Miss-Status Holding Register
Check L2 Cache
Check Global Memory
L1 Cache
MSHR
L1 Cache
MSHR
GPU Core
PE
PE
LD/ST Unit
Coalescing Unit
…
PE
PE
LD/ST Unit
Coalescing Unit
GPU Core
…
…
Interconnect (NoC)
Global Memory (DRAM)
L2 Cache
MSHR

## Slide 16: Conventional Cache/NoC Hierarchy
Network-on-Chip (NoC)
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
Core
Core
L1
Core
L1
Core
L1
Core
L1
Reply
77% cores requests
served @ L2
High queueing delay
1 L1 bandwidth is underutilized
& L2 bandwidth is a bottleneck!
Pattnaik, et al. “Opportunistic Computing in GPU Architectures.” ISCA’19.
2 Replication of data (cache line) across L1 caches
L1
L1
Private
L1
L2
Memory
L2
Memory
L2
Memory
L2
Memory
L2

## Slide 17: Why Replication? Breadth First Search (BFS)
Assume node 0 and 1 are processed by different cores.
Li, et al. “Inter-Core Locality Aware Memory Scheduling.” CAL’15.
Accessing Shared Data Structures  Data Replication
Core A
0
2
Core B
1
2
Node
0
Node
1
Node
2

## Slide 18: Volume of Replication
Fraction of the L1 read misses that can be satisfied by ≥ 1 remote core.
Chart: 
| BLK | LIB | NQU | SLA | FWT | JPEG | AES | Kmeans | FDTD-2D | STO | SC | RAY | BP | TRA | GEMM | HS | 3MM | Stencil2D | CONS | NW | LPS | 2MM | LUD | SYRK | BFS | QTC | BFS2 | 3DCONV | CFD | 2DCONV | Scan | Triad | Reduction | ResNet | SqueezeNet | NN | AlexNet
Inter-core Locality | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.012195 | 0.019606 | 0.027679 | 0.027695 | 0.045782 | 0.063055 | 0.12907 | 0.14632 | 0.15332 | 0.17311 | 0.18809 | 0.25022 | 0.27491 | 0.28012 | 0.31143 | 0.36036 | 0.41327 | 0.41908 | 0.46964 | 0.51465 | 0.55088 | 0.55165 | 0.57262 | 0.64656 | 0.87591 | 0.90339 | 0.90601 | 0.91116 | 0.95423
Replication Volume
Replication Ratio = 95%
Replica Count = 22

## Slide 19
Can be utilized as a source of bandwidth
Can be viewed as a waste of cache capacity
Data Replication
More Replication = Sources of Bandwidth
Zero Replication =
More Capacity
PACT’19
PACT’20, HPCA’21

## Slide 20: Outline
Conventional Cache/Interconnect Hierarchy
Dissertation Research
  Exploiting Data Replication
    Unlocking Remote-core Bandwidth in GPUs
  Eliminating/Reducing Data Replication
    A Case for Shared L1 Caches in GPUs
    Aggregated Decoupled Caches for GPUs
Conclusions & Future Work

## Slide 21: Dissertation Research
Exploiting Data Replication
Remote-core Bandwidth
[PACT 2019]
Analyzing and Leveraging Remote-core Bandwidth for Enhanced Performance in GPUs
Mohamed Assem Ibrahim, Hongyuan Liu, Onur Kayiran, Adwait Jog

## Slide 22: Let's Bake Cookies!
Ingredients:
  Peanut Butter
  Sugar
  Eggs
  Chocolate Chips
Neighbors = Additional Source of Ingredients!

## Slide 23: Remote-core Bandwidth
Use Remote Cores
(as additional bandwidth source)
Replication/Sharing of Data across Cores
Network-on-Chip
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
Core
Core
L1
Core
L1
Core
L1
Core
L1
L2
Memory
L2
Memory
L2
Memory
L2
Memory
Request
Reply
Efficient Inter-core Communication
Reply
L1
L1
Request
A
B
L2

## Slide 24: Challenges?
Which data is shared?
  Not every cache line is shared across cores
Not all PCs (program
counter) are equal!
PC-based Sharing Predictor

## Slide 25: Challenges?
Which remote cores have the shared data?
  Not every core has the shared data
Not all remote cores are equal!
Supplier-based Core Selector

## Slide 26: Challenges?
How to fetch the shared data?
  Send parallel probes
Two-level Probing
Redundant replies!
Leader
Scout
Scout
Scout

## Slide 27: Evaluation
Results are normalized to Baseline (no inter-core communication).
Under an impaired NoC with a single virtual channel.
  Average = 10%, Max = 26%
  With 4 shallow virtual channels  Average = 21%, Max = 53%
Chart: 
| C-BFS | C-NN | C-BFS2 | R-CFD | S-SpMV | L-BH | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM | Mean
RP | 1.2072 | 1.0418 | 1.2564 | 1.0596 | 1.022 | 1.0483 | 1.0975 | 1.0885 | 1.134 | 1.0961 | 1.0319 | 1.0963
10%
Chart: Normalized IPC
| C-RAY | R-BFS | S-MD | L-SSSP | P-BICG | Mean
RP(5,2,0.5) | 0.96054 | 0.99107 | 0.99052 | 0.99853 | 0.99735 | 0.9875
<1%
Drop
Handle the absence of data replication without degrading performance!

## Slide 28: Outline
Conventional Cache/Interconnect Hierarchy
Dissertation Research
  Exploiting Data Replication
    Unlocking Remote-core Bandwidth in GPUs
  Eliminating/Reducing Data Replication
    A Case for Shared L1 Caches in GPUs
    Aggregated Decoupled Caches for GPUs
Conclusions & Future Work

## Slide 29: Dissertation Research
Eliminating/Reducing Data Replication
Shared L1 Caches
[PACT 2020]
Analyzing and Leveraging Shared L1 Caches in GPUs
Mohamed Assem Ibrahim, Onur Kayiran, Yasuko Eckert,
Gabriel H. Loh, Adwait Jog

## Slide 30: Let's Bake Cookies!
Ingredients:
  Peanut Butter
  Sugar
  Eggs
  Chocolate Chips
Agree that each one of us will buy and keep one type only!
No Replication = Additional Ingredients in the Building!

## Slide 31: Shared L1 Caches
Network-on-Chip
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
Core
Core
L1
Core
L1
Core
L1
Core
L1
L1
L1
Private L1
L2
Memory
L2
Memory
L2
Memory
L2
Memory
L2
= Replication of L1 Data across Cores
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Full Addr.
Range
Shared L1
Addr.
Range A0
Addr.
Range A1
Addr.
Range A2
Addr.
Range A3
…
…
…
…
…
…
Addr.
Range An-2
Addr.
Range An-1
= Replication Eliminated!
Reply
Request
Req.
Core
Home
Core
Efficient Inter-core Communication
Unique Addr. Range Slice
Do not Cache!

## Slide 32: Shared L1 Caches
Chart: 
| C-BFS | C-BFS2 | R-CFD | R-LUD | S-QTC | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM | Mean
Shared | 0.97191 | 0.69718 | 1.0839 | 1.0943 | 0.75404 | 1.1836 | 0.81393 | 1.1487 | 1.0999 | 0.85488 | 0.86512 | 0.9464
Chart: 
| C-BFS | C-BFS2 | R-CFD | R-LUD | S-QTC | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM | Mean
Shared | 0.31043 | 0.3973 | 0.22256 | 0.047491 | 0.91146 | 0.11617 | 0.16859 | 0.32525 | 0.31524 | 0.095152 | 0.082239 | 0.19832
Eliminate Replication  Lower L1 Miss Rate
Performance drops by 5%!
Naïve Communication  2.2X Latency Overhead
80%
Drop
5%
Drop
Solution?

## Slide 33: Optimized Shared L1 Caches Reduce Wasted NoC Bandwidth
Chart: 
| C-BFS | C-BFS2 | R-CFD | R-LUD | S-QTC | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM
Access=32 | 461325 | 586247 | 505430 | 0 | 924217 | 0 | 190054 | 177952 | 157586 | 168817 | 143755
Access=64 | 24781 | 13598 | 29963 | 56607 | 454 | 0 | 0 | 0 | 0 | 0 | 0
Access=128 | 132343 | 175971 | 184535 | 0 | 779 | 328824 | 126182 | 259932 | 123985 | 125942 | 113010
32B | 32B | 32B | 32B
Cache Line
Chunking
Reply from Home only has requested data by the Requester.

## Slide 34: Optimized Shared L1 Caches Shared++
Chart: 
| C-BFS | C-BFS2 | R-CFD | R-LUD | S-QTC | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM | Mean
Shared+Chunk+Min(H,L2) | 1.3957 | 1.3583 | 1.5558 | 1.082 | 1.203 | 1.3681 | 1.1673 | 1.4517 | 1.1593 | 1.0709 | 1.1825 | 1.2632
Chart: 
| C-BFS | C-BFS2 | R-CFD | R-LUD | S-QTC | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM | Mean
Shared+Chunk+Min(H,L2) | 0.22159 | 0.32386 | 0.25744 | 0.072017 | 0.78647 | 0.07318 | 0.34156 | 0.35846 | 0.3168 | 0.18598 | 0.1534 | 0.22756
Eliminate Replication  Lower L1 Miss Rate
Performance improves by 26%!
Optimized Communication  9% Latency Overhead
Replication-insensitive
Applications?

## Slide 35: Handling Private-friendly Applications
Collect counters.
Check end of phase.
Evaluate metrics.
Choose Shared or Private cache organization.
Execute with chosen organization.
Check end of phase.
Sampling Phase
Execution Phase

## Slide 36: Handling Private-friendly Applications Sampling Phase
Set
Request Address
Set 0
Set 1
Set 2
Set 3
Set 4
Set 5
. .
Set 30
Set 31
L1 Cache
LSB of Set bits
Legend
Sets treated as Shared
Sets treated as Private
Private Stats
Local L1 Requests
L1 Requests
L1 Misses
Replies from L2
Replies from Homes
Counters
Shared Stats
Local L1 Requests
L1 Requests
L1 Misses
Replies from L2
Replies from Homes
Counters
Core
0?
Even
Odd
Sampling
Completed?
Yes
Evaluate Sampling Stats
Private or Shared
DynEB  Effective BW (EB)
BW-based Metric
EB IPC
Local
Wang, et al. “Efficient and Fair Multi-programming in GPUs via Effective Bandwidth Management.” HPCA’18.

## Slide 37: Evaluation IPC
Chart: 
| C-BFS | C-BFS2 | R-CFD | R-LUD | S-QTC | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM | Mean
Shared++ | 1.3957 | 1.3583 | 1.5558 | 1.082 | 1.203 | 1.3681 | 1.1673 | 1.4517 | 1.1593 | 1.0709 | 1.1825 | 1.2632
DynEB | 1.3228 | 1.3202 | 1.5231 | 1.0662 | 1.1127 | 1.3408 | 1.1699 | 1.4137 | 1.096 | 1.0499 | 1.1045 | 1.2198
Chart: 
Shared++ | 0.48512 | 0.63534 | 0.72796 | 0.7984 | 0.87639 | 0.96621 | 0.97863 | 0.98662 | 0.98925 | 0.99582 | 1.0002 | 1.0035 | 1.0052 | 1.0133 | 1.0678 | 1.0709 | 1.082 | 1.1397 | 1.1593 | 1.1673 | 1.1825 | 1.196 | 1.203 | 1.3583 | 1.3681 | 1.3957 | 1.4517 | 1.5558
DynEB | 0.91666 | 0.92125 | 0.98024 | 0.99091 | 0.9913 | 0.99474 | 0.99674 | 0.99759 | 1 | 1 | 1.003 | 1.0033 | 1.004 | 1.0106 | 1.0499 | 1.0662 | 1.0728 | 1.096 | 1.1045 | 1.1127 | 1.1699 | 1.2264 | 1.2483 | 1.3202 | 1.3228 | 1.3408 | 1.4137 | 1.5231
Chart: Normalized IPC
| C-RAY | C-TRA | C-NN | S-SpMV | S-BFS | Mean
Shared++ | 0.87639 | 0.7984 | 0.48512 | 0.63534 | 0.72796 | 0.69052
DynEB | 0.99674 | 0.91666 | 0.92125 | 0.9913 | 0.99091 | 0.96268
Chart: Normalized IPC
| C-BFS | C-BFS2 | R-CFD | R-LUD | S-QTC | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-GEMM | Mean
Shared++ | 1.3957 | 1.3583 | 1.5558 | 1.082 | 1.203 | 1.3681 | 1.1673 | 1.4517 | 1.1593 | 1.0709 | 1.1825 | 1.2632
DynEB | 1.3228 | 1.3202 | 1.5231 | 1.0662 | 1.1127 | 1.3408 | 1.1699 | 1.4137 | 1.096 | 1.0499 | 1.1045 | 1.2198
Results are normalized to Private L1 organization baseline.
Replication-sensitive Applications  Average = +22%, Max = +53%
Private-friendly Applications  Average = -4%
22%
Private-friendly
Replication-sensitive

## Slide 38: Outline
Conventional Cache/Interconnect Hierarchy
Dissertation Research
  Exploiting Data Replication
    Unlocking Remote-core Bandwidth in GPUs
  Eliminating/Reducing Data Replication
    A Case for Shared L1 Caches in GPUs
    Aggregated Decoupled Caches for GPUs
Conclusions & Future Work

## Slide 39: Dissertation Research
Eliminating/Reducing Data Replication
Decoupled L1 Caches
[HPCA 2021]
Analyzing and Leveraging Decoupled L1 Caches in GPUs
Mohamed Assem Ibrahim, Onur Kayiran, Yasuko Eckert,
Gabriel H. Loh, Adwait Jog

## Slide 40: Let's Bake Cookies!
Need a way to communicate
with my neighbors.
Disrupt my neighbors!
Ingredients:
  Peanut Butter
  Sugar
  Eggs
  Chocolate Chips
Agree that each one of us will buy and keep one type only!
Solution?
Remove the fridge from each apartment.
Put them in a common area.

## Slide 41: Conventional Cache/NoC Hierarchy
Improving L1 bandwidth utilization requires:
  NoC overhead to enable inter-core communication.
    Under both 2D mesh and crossbar!
  Disrupting the Home core.
    Arbitration between local and remote requests.
Core
L1
L2
Memory
NoC
Problem Source: Tightly-coupled GPU core and L1 cache!
Solution?

## Slide 42: Decoupled L1 Caches (DC-L1s)
A-1
A-2
Separate L1 cache from the GPU core.
  Break the tight-coupling!
0
1
2
…
NoC#1 (Core ↔ DC-L1)
NoC#2 (DC-L1 ↔ L2)
3
4
5
A-1
A-2
0
1
2
…
3
4
5
0
1
2
…
3
4
5
C-1
C-2
Lite GPU Core
(No L1 Cache)
DC-L1
(Decoupled L1)
L2+Memory
Level-1
Cache
Level-2
Cache
Two-level Cache
Hierarchy

## Slide 43: Aggregating DC-L1 Caches
2X
Size
0
Merge X DC-L1s to form one bigger DC-L1 cache.
  Reduced replication
  Better L1 bandwidth utilization
  Lower peak L1 bandwidth
L2
Lite Core
DC-L1
0
1
0
…
0
1
…
40x32 XBar
2x1 XBar
2
3
1
2x1 XBar
…
…
2x1 XBar
2x1 XBar
39
38
2
78
79
31
30
Aggregation Granularity?
1
Example of aggregating two DC-L1s.

## Slide 44: Aggregation Granularity
Metric | Low Aggregation | High Aggregation
Replication Volume |  | 
Peak L1 Bandwidth |  | 
NoC Area/Power |  | 

## Slide 45: Aggregation Granularity Verdict
Pr40: Aggregate two DC-L1s into one 2X DC-L1.
  IPC = 15% boost
  NoC Area = 28% lower
  NoC Power = 4% lower
  L1 Miss Rate = 19% lower  High Replication!
Shared DC-L1s?

## Slide 46: Shared DC-L1 Caches
39
38
2X
Size
Shared cache organization across DC-L1s.
  Eliminate replication.
Use 80x40 crossbar in NoC#1.
  Enable communication between a given core to all DC-L1 caches.
L2
Lite Core
DC-L1
0
1
0
…
0
1
…
40x32 XBar
80x40 XBar
2
3
1
…
2
78
79
31
30
Unique Addr. Range Slice
Assume 80-core System with 40 DC-L1s
(Aggregation Granularity = 2).

## Slide 47: Shared DC-L1 Caches Verdict
Sh40: 40 aggregated and shared DC-L1s under 80-core system.
  IPC = 48% boost
  L1 Miss Rate = 89% lower = Replication Eliminated!
  NoC Area = 69% higher
  NoC Power = 57% higher
Clustered Shared DC-L1s?
Replication-insensitive
Applications?

## Slide 48: Clustered Shared DC-L1 Caches
37
36
39
38
0
3
1
2
…
…
37
36
39
38
Shared cache organization across a cluster of DC-L1s.
  Eliminate replication within a cluster.
  Limit overall replication.
Use smaller crossbars in NoC#1.
  Enable communication between a given core to all DC-L1 caches in a cluster.
L2
Lite Core
DC-L1
0
1
…
0
1
…
10x8 XBar
8x4 XBar
7
…
…
8x4 XBar
7
31
24
Clusters Count?
…
…
Assume 80-core System with 40 DC-L1s.
Unique Addr. Range Slice
79
72
73
Choose 10 Clusters (Sh40+C10)
IPC Boost + Replication Reduction + Reduced Area/Power
10x8 XBar
C0
C1
C2
C3
C9
C0
C1
C2
C3
C9
2
25
26
1
0
3
2
31
24
25
26
7
0
1
2

## Slide 49: Frequency-boost Optimization
Smaller Crossbars = Higher Operating Frequency
Optimization  Double the NoC frequency in NoC#1
0
1
0
8x4 XBar
7
3
1
…
2
Chart: Crossbar
| 2x1 | 8x4 | 40x32 | 80x32 | 80x40
Max. Freq (MHz) | 3533.0071 | 2240.3943 | 799.335 | 496.4257 | 483.992
Sh40+C10+Boost

## Slide 50: Evaluation IPC
Chart: 
Pr40 | 0.66185 | 0.79764 | 0.80615 | 0.83434 | 0.8682 | 0.86991 | 0.89487 | 0.89769 | 0.93186 | 0.93234 | 0.93889 | 0.94952 | 0.95139 | 0.95606 | 0.95874 | 0.9642 | 0.96505 | 0.96651 | 0.98474 | 0.99167 | 1.0011 | 1.0079 | 1.2164 | 1.296 | 1.3959 | 1.6081 | 1.668 | 1.9992
Sh40 | 0.15289 | 0.48809 | 0.52723 | 0.55583 | 0.60381 | 0.95583 | 0.96512 | 0.96746 | 0.97026 | 0.97227 | 0.98259 | 0.99167 | 0.99614 | 1.0546 | 1.0588 | 1.06 | 1.0803 | 1.1503 | 1.2068 | 1.2382 | 1.2587 | 1.298 | 1.396 | 1.6059 | 1.638 | 1.9341 | 2.3611 | 2.9459
Sh40+C10+Boost | 0.86313 | 0.90708 | 0.93805 | 0.94744 | 0.94874 | 0.96871 | 0.96974 | 0.97895 | 0.9902 | 0.9925 | 0.99659 | 1.0078 | 1.0139 | 1.0164 | 1.0179 | 1.0325 | 1.132 | 1.2072 | 1.2877 | 1.2884 | 1.3145 | 1.3203 | 1.3501 | 1.4372 | 1.9582 | 2.0575 | 5.0231 | 8.0233
Chart: 
| C-RAY | C-NN | P-2DCONV | P-3MM | P-GEMM | Mean
Pr40 | 0.8682 | 0.79764 | 0.66185 | 0.86991 | 0.83434 | 0.80242
Sh40 | 0.15289 | 0.55583 | 0.48809 | 0.60381 | 0.52723 | 0.42087
Sh40+C10+Boost | 0.90708 | 0.94874 | 0.94744 | 0.9902 | 0.93805 | 0.94593
Chart: 
| C-BFS | C-BFS2 | R-CFD | S-QTC | S-Reduction | S-Triad | P-3DCONV | P-2MM | P-SYRK | T-AlexNet | T-ResNet | T-SqueezeNet | Mean
Pr40 | 0.9642 | 0.89487 | 0.98474 | 0.93234 | 0.80615 | 0.89769 | 0.93186 | 1.668 | 1.3959 | 1.9992 | 1.296 | 1.6081 | 1.147
Sh40 | 1.396 | 1.2382 | 1.2587 | 1.6059 | 1.2068 | 1.1503 | 0.97227 | 1.06 | 2.3611 | 2.9459 | 1.638 | 1.9341 | 1.4797
Sh40+C10+Boost | 1.4372 | 1.3501 | 1.3203 | 1.2884 | 0.86313 | 1.2072 | 1.3145 | 1.9582 | 1.132 | 8.0233 | 2.0575 | 5.0231 | 1.7511
Chart: 
| C-BLK | C-LIB | C-LPS | C-NQU | C-RAY | C-STO | C-SLA | C-CONS | C-FWT | C-TRA | C-BFS | C-NN | C-JPEG | C-BFS2 | C-AES | C-Kmeans | R-BP | R-BFS | R-HS | R-CFD | R-SC | R-NW | R-LUD | S-QTC | S-Reduction | S-Scan | S-Stencil2D | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-FDTD-2D | P-GEMM | P-SYRK | T-AlexNet | T-ResNet | T-SqueezeNet | Mean | Mean | Mean
Pr40 | 0.95874 | 0.94952 | 0.95139 | 0.99167 | 0.8682 | 0.90903 | 0.97548 | 0.94317 | 1.0011 | 0.91094 | 0.9642 | 0.79764 | 0.92637 | 0.89487 | 0.95606 | 0.78165 | 0.93889 | 0.91327 | 0.96651 | 0.98474 | 1.2164 | 1.0079 | 0.96505 | 0.93234 | 0.80615 | 0.94839 | 0.87171 | 0.89769 | 0.66185 | 0.93186 | 1.668 | 0.86991 | 0.9672 | 0.83434 | 1.3959 | 1.9992 | 1.296 | 1.6081 | 0.9872 | 1.147 | 0.92118
Sh40 | 0.98259 | 0.95583 | 1.0803 | 0.99167 | 0.15289 | 0.89871 | 0.99194 | 1.0161 | 0.99614 | 1.0828 | 1.396 | 0.55583 | 0.93071 | 1.2382 | 0.96512 | 0.96611 | 0.97026 | 0.89667 | 1.0588 | 1.2587 | 1.298 | 1.0546 | 0.96746 | 1.6059 | 1.2068 | 1.3426 | 0.91761 | 1.1503 | 0.48809 | 0.97227 | 1.06 | 0.60381 | 0.96123 | 0.52723 | 2.3611 | 2.9459 | 1.638 | 1.9341 | 1.0155 | 1.4797 | 0.85352
Sh40+C10+Boost | 0.97895 | 0.96974 | 1.0164 | 0.99659 | 0.90708 | 0.94715 | 0.97941 | 0.98743 | 1.0139 | 0.9655 | 1.4372 | 0.94874 | 0.95581 | 1.3501 | 1.0078 | 0.85986 | 0.96871 | 0.95825 | 1.0325 | 1.3203 | 1.2877 | 1.0179 | 0.9925 | 1.2884 | 0.86313 | 1.1037 | 0.89901 | 1.2072 | 0.94744 | 1.3145 | 1.9582 | 0.9902 | 0.93315 | 0.93805 | 1.132 | 8.0233 | 2.0575 | 5.0231 | 1.1788 | 1.7511 | 0.98205
Results are normalized to Private L1 organization baseline.
Replication-sensitive Applications  Average = +75%, Max = +8X
Poor-performing Applications  Average = -5%
Poor-performing
Replication-sensitive
8x
5x
75%

## Slide 51: Outline
Conventional Cache/Interconnect Hierarchy
Dissertation Research
  Exploiting Data Replication
    Unlocking Remote-core Bandwidth in GPUs
  Eliminating/Reducing Data Replication
    A Case for Shared L1 Caches in GPUs
    Aggregated Decoupled Caches for GPUs
Conclusions & Future Work

## Slide 52: Conclusions
Goal: To support the continuous scaling of compute throughput, it is crucial to conserve and improve on-chip memory bandwidth utilization.
Direction: Analyze and leverage data replication across the L1 caches to improve their utilization and boost on-chip bandwidth.
Contributions:
  [PACT’19] Develop probing mechanisms to efficiently unlock remote-core bandwidth, an additional source of bandwidth in GPUs.
  [PACT’20] Propose a renovated cache design that enables both private and shared cache organization for L1 cache.
  [HPCA’21] Propose co-designing the cache hierarchy and the interconnect and present DC-L1 cache, an L1 cache decoupled from the GPU core.

## Slide 53: Future Research Directions
Short-term: Improve on-chip bandwidth utilization by considering other bandwidth sources
  How to leverage data replication between the L1 and L2 caches?
  How to leverage value locality and predictability to extend the scope of data replication?

## Slide 54: Future Research Directions
Long-term: Investigate graphics pipeline & workloads
  Critical from business & research perspectives
  Goals:
    Profile & Analyze graphics workloads
    Understand & Optimize the underlying hardware

## Slide 55: Timeline
[Spring’16]
Joined William & Mary + Started working with Prof. Adwait Jog
[Fall’17]
Passed Ph.D. Candidacy
[Fall’19]
Dissertation Proposal
Today
[Spring’21]
Dissertation Defense
[Spring’21]
Postdoc @ AMD Research
[Summer’18]
Internship @ AMD Research
[Summer + Fall’20] Internship @ AMD Research

## Slide 56: Publication List
[PACT’19] Mohamed Assem Ibrahim, Hongyuan Liu, Onur Kayiran, Adwait Jog Analyzing and Leveraging Remote-core Bandwidth for Enhanced Performance in GPUs
[PACT’20] Mohamed Assem Ibrahim, Onur Kayiran, Yasuko Eckert, Gabriel Loh, Adwait Jog Analyzing and Leveraging Shared L1 Caches in GPUs
[HPCA’21] Mohamed Assem Ibrahim, Onur Kayiran, Yasuko Eckert, Gabriel Loh, Adwait Jog Analyzing and Leveraging Decoupled L1 Caches in GPUs

## Slide 57: Publication List
[ICS’19] Haonan Wang, Mohamed Assem Ibrahim, Sparsh Mittal, Adwait Jog Address-Stride Assisted Approximate Value Prediction in GPUs
[MICRO’18] Hongyuan Liu, Mohamed Assem Ibrahim, Onur Kayiran, Sreepathi Pai, Adwait Jog Architectural Support for Efficient Large-Scale Automata Processing
[HPCA’18] Haonan Wang, Fan Luo, Mohamed Assem Ibrahim, Onur Kayiran, Adwait Jog Efficient and Fair Multi-programming in GPUs via Effective Bandwidth Management
[HPCA’17] Xulong Tang, Ashutosh Pattnaik, Huaipan Jiang, Onur Kayiran, Adwait Jog, Sreepathi Pai, Mohamed Assem Ibrahim, Mahmut T. Kandemir, Chita R. Das Controlled Kernel Launch for Dynamic Parallelism in GPUs

## Slide 58
Thank You!

## Slide 59: Thanks to all the committee members and audience!

## Slide 60: Rethinking Cache Hierarchy and Interconnect Design for Next-generation GPUs
Mohamed Assem Ibrahim
Ph.D. Candidate
https://massemibrahim.github.io/
Questions?